Notes
For a 16-bit CRC, the polynomial 0xBAAD provides Hamming Distance 4 protection for messages up to 2048 bytes (see Koopman, Philip, "Better Embedded System Software", also https://betterembsw.blogspot.com/2010/05/whats-best-crc-polynomial-to-use.html). The value 0xBAAD represents the polynomial in "Koopman notation" (i.e., reverse of reciprocal with trailing +1 omitted). The "normal" representation would be 0x755B. Since RS-232 is little-endian (transmitted lsb first), Aeon's CRC generation and validation code works the data in that direction, i.e., it shifts to the right instead of left, and accordingly uses the reverse version of the polynomial, 0xDAAE. Additionally, to detect potential errors in leading zero bits, a preset of -1 (0xFFFF) is used instead of 0, and similarly for potential trailing zero errors, the CRC code is inverted before appending it to the message. The resulting residual constant, 0x82C0, is used by all Aeon serial devices.

Additionally, all Aeon serial device response messages are terminated with a two-byte CRC code followed by ETX {0x03}. All command messages must also be terminated with a two-byte CRC code followed by ETX. Finally, except as a terminating character, and possibly as a byte in the CRC code, ETX may not appear in any message.

The following algorithms efficiently handle encoding, transmitting, receiving and decoding messages according to the foregoing conventions.

///////////////////////////////////////////////////////
// CRC algorithms / pseudocode
//

// global constants
const UInt16 CRC_POLY = 0xDAAE	// reversed version
const UInt16 CRC_INIT = 0xFFFF	// preset = -1
const UInt16 CRC_GOOD = 0x82C0	// residual constant
const byte ETX = 0x03;

// reception

// global variables for reception
UInt16 rxCRC;
byte_sequence rxMessage;
bool ErrorCRC;
int bwuETX; // bytes with unexpected ETX

// rxInit() must be called once before rxByte is called the first time
rxInit()
{
rxCRC = CRC_INIT;
rxMessage = "";
CRC_Error = false;
bwuETX = 0;
}
// call for each received byte c
rxByte(byte c)
{
if (bwuETX > 0) bwuETX++;
if (c == ETX)
{
if (rxCRC == CRC_GOOD)
{
// place the validated message into a message handler queue
// e.g., (first removing the trailing CRC code)
enqueueMessage(left(rxMessage, rxMessage.Length-2));
}
else if (bwuETX == 0)
{
bwuETX = 1;
}

if (rxCRC == CRC_GOOD || CRC_Error)
{
rxInit();	// start fresh on the next byte
return; // continue with the next byte
}
}
rxCRC = CRC_Update(rxCRC, c);
rxMessage += c;
if (!CRC_Error && bwuETX > 2)
CRC_Error = true; // also insert any CRC error handling here
}

// transmission

// global variables for transmission
UInt16 txCRC;

// txInit() must be called once before txByte is called the first time
txInit()
{
txCRC = CRC_INIT;
}
// call once for each data byte of the message to be transmitted
// call with c = ETX after the last data byte of the message
txByte(byte c)
{
if (c == ETX)
{
txCRC = ~txCRC;	// post-invert
send(LOWBYTE(txCRC));	// transmit the CRC code's low byte first
send(HIGHBYTE(txCRC));
txCRC = CRC_INIT;	// reset the CRC code
}
else
{
txCRC = CRC_Update(txCRC, c);
}
send(c);	// send the byte
}

// utility function

UInt16 CRC_Update(UInt16 crcCode, byte b)
{
crcCode ^= b;
for (int bit = 0; bit < 8; bit++)
{
int lsb = crcCode & 1;
crcCode >>= 1;
if (lsb != 0) crcCode ^= CRC_POLY;
}
return crcCode;
}